## Slide 1
Web interface
  Scenario editor
    Scenario met 4 tijden per dag, 7 dagen per week.
    Kleur per tijd instelbaar
  Config
    Gebruik thuis aan Wifi netwerk (SSID, wachtwoord)
    Gebruik elders met Oli netwerk
    Access Point en Station mode (tegelijkertijd)
  Status
    Verbonden netwerk
    Gebruikers handleiding
  Kleurkiezer
Tijd
  real-time clock
  Zomer en wintertijd (Europa)
  Automatische synchronisatie met tijdserver als verbonden met internet
Reset naar fabrieksinstellingen met schakelaar of via web
Licht-uit/aan met schakelaar
Doorschakelen naar volgend scenario met schakelaar, hoe om je weer op de oude instelling? Bij de volgende trigger.
Over the air update
Aanpasbaar oli wachtwoord
QR-code voor Wifi en web-pagina’s
Geen https
What to do with RTC that has lost battery power

## Slide 2
Mode: APSTA
SSID: Oli
Initial password: 8 digit SSID/PW printed on Oli
User connects to WiFi AP with Password
Set
day/hh/mm
new password for user Oli
Reset to factory settings
Set
Your WiFi SSID
Your WiFi password
Connect to Your WiFi
Hostname: Oli.local
IP-address: DHCP
no https
User connects to Your WiFi with Password
http://oli.local
http://192.168.x.y
no https
http://oli.local
http://192.168.4.1
Create scenario per day
Store scenario
ButtonX press 5 seconds
Initial power-on
power-on
APSTA-mode
power-on
APSTA-mode
Clear: Your-SSID, Your-PW and Scenario’s
Create scenario per day
Store scenario
Switch LEDs off
ButtonX short press
Light-show
ButtonX short press
Back to normal
Real-time clock powered by battery
Day/hh/mm
Color/Intensity
Off
Execute scenarios
Manage summer & wintertime
Installation
Execution
Show config
Day/hh/mm
WiFi SSID
URL http://oli
Lamp color/intensity
Reset to default
Show scenarios
For 7 days:
For 5 moments:
hh/mm
Lamp color/intensity
Failed to connect
1xRed blink
power-on
Not configured
LED1: Soft red color
Time configured
Soft yellow color
Scenarios configured
Config
Status
Scenarios
Oli Webpages
Kleur kiezer
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
❌
❌

## Slide 3
AP=true
STA=false
AP=false
STA=false
Start_AP
AP=true
TO & APchanged
stopAP, startAP
AP=true
AP=x STA=false connecting
TO & STA credentials
startSTA
STA connect fails
If AP=false: startAP
AP=true
STA=true
AP=true
AP=true & Connected
STA=true
STA=true
AP=false
TO & STA=true
stopAP
AP=false
TO
[STA Connect lost || STA credentials change]
stopSTA
STA=false
startSTA
AP=false
STA=false
STA credentials
startAP
AP=true
startSTA
STA credentials
& STAchanged
startSTA
AP=false & Connected
STA=true

## Slide 4: States & Errors
States (regenboog kleuren)
  Initial LED uit
  ??? paars
  Kleurentester blauw
  On-line – in sync == STA-mode groen
  On-line – no sync == STA-mode geel
  Off-line – no WiFi == AP-Mode oranje
Errors – pulserend bij opstarten
  HW – error 15 x blink rood [RTC not found]
  OTA – error 15 x blink oranje

## Slide 5: How to get the correct time?
RTC library: https://github.com/PaulStoffregen/DS1307RTC
Time library: https://github.com/PaulStoffregen/Time
TimeZone library: https://github.com/JChristensen/Timezone
Arduino interne tijd is niet accuraat  gebruik RTC en sync Arduino iedere 5 minuten met de RTC , dit doet de Time library  die gebruiken we niet
Zet alle tijd sources in UTC tijd (RTC en NTP)
Sync RTC met NTP als NTP tijd beschikbaar komt
Gebruik de TZ library voor zomertijd aanpassing
WiFi not connected  gebruik de UTC tijd van de RTC
WiFi connected  start NTP en vraag om de UTC Tijd
  If NTP time is available: If RTC != NTP  update RTC

## Slide 6: Time (2)
Always focus on Coordinated Universal Time (UTC)
  Make NTP and RTC keep UTC time.
  UTC is not a Timezone but a time standard
Always use the RTC as time source
Keep RTC in sync with NTP
NTP happens to update the systemtime
Use standard C functions:
  time() get system time
  ctime() convert time_t (seconds-since-1970) to date string

## Slide 7
NTP server #include <ESP8266WiFi.h> declaration: const char* ntpServer = "pool.ntp.org"; setup: configTime(gmtOffset_sec, daylightOffset_sec, ntpServer); struct tm timeinfo; loop: struct tm timeinfo; getLocalTime(&timeinfo);
Time library #include <TimeLib.h> Internal system time is based on the standard Unix time_t. The value is the number of seconds since Jan 1, 1970. System time begins at zero when the sketch starts. breakTime(time, &tm); // break time_t into elements stored in tm struct makeTime(&tm); // return time_t from elements stored in tm struct Time Library needs a sync function specified: Setup: setSyncProvider(RTC.get); // the function to get the time from the RTC RTC.get which returns a time_t value. time_t get tmElements_t tm; …. makeTime(tm)
Combine ESP NTP server with Time library setSyncProvider(NTPgetTime); time_t NTPgetTime() { getLocalTime(&timeinfo); return(makeTime(timeinfo); }

## Slide 8: Open issues
Test WiFi statemachine as I changed the initial state
What to do with RTC that has lost battery power
Update Config page for timing stuff
⁉️